## Slide 1: Dycore Rewrite
Tobias Gysi

## Slide 2: Status dycore rewrite
Status a year ago
Development of a stencil library
CPU rewrite of the COSMO dycore (HP2C dycore)
Functional
Stencil library GPU backend
Tracer advection & diffusion
Fortran integration of HP2C dycore
Multi node support (see Carlo’s presentations)
Non periodic boundary condition support
Ongoing
Implement non periodic boundary conditions in the dycore

## Slide 3: Stencil computations
Why are we interested in stencils?
Dominating algorithmic motif within the COSMO dycore
Stencil Definition
Kernel updating array elements according to a fixed access pattern
Example 2D Laplacian
lap(i,j,k) = –4.0 * data(i,j,k) +
data(i+1,j,k) + data(i-1,j,k) +
data(i,j+1,k) + data(i,j-1,k);

## Slide 4: Stencil library development
Motivation
Provide a way to implement stencils in a platform independent way
Hide complex / “ugly” optimizations from the library user
 Single source code which is performance portable
Technology
C++ library using template meta programming
Optimized back-ends for GPU and CPU
 | CPU | GPU
Storage Order (Fortran) | KIJ | IJK
Parallelization | OpenMP | CUDA

## Slide 5: Stencil code concepts
DO k = 1, ke
DO j = jstart, jend
DO i = istart, iend
lap(i,j,k) =
-4.0 * data(i,j,k) +
data(i+1,j,k) + data(i-1,j,k) +
data(i,j+1,k) + data(i,j-1,k)
ENDDO
ENDDO
ENDDO
A stencil definition consists of 2 parts
Loop-logic: Defines stencil application domain and execution order (green)
Update-function: Expression evaluated at every location (blue)
loop-logic
update-function / stencil
While the loop-logic is platform dependent the update-function is not  treat the two separately

## Slide 6: Loop-Logic expressed using a DSEL
Define a DSEL (Domain specific embedded language) in C++
Code is implemented as a type
Type is translated into sequence of operations (DSEL compilation)
Operation objects (“code fragments”) are used to generate the code (there are pre-packaged loop objects for CPU and GPU)
 All this is going on at compile time (template meta-programming) which allows us to generate platform dependent loop code
Loop object library
ApplyBlocks
OpenMP
LoopOverBlock
OpenMP
LoopOverBlock
CUDA
ApplyBlocks
CUDA
DSEL loop definition
(C++ type)
Platform dependent loop code
Compiler
LoopOverBlock
CUDA
ApplyBlocks
CUDA
Motivation to use C++

## Slide 7: Putting it all together
enum { data, lap };
template<typename TEnv>
struct Lap
{
STENCIL_STAGE(TEnv)
STAGE_PARAMETER(FullDomain, data)
STAGE_PARAMETER(FullDomain, lap)
static void Do(Context ctx, FullDomain)
{
ctx[lap::Center()] =
-4.0 * ctx[data::Center()] +
ctx[data::At(iplus1)] +
ctx[data::At(iminus1)] +
ctx[data::At(jplus1)] +
ctx[data::At(jminus1)];
}
};
IJKRealField lapfield, datafield;
Stencil stencil;
StencilCompiler::Build(
stencil,
"Example",
calculationDomainSize,
StencilConfiguration<Real, BlockSize<32,4> >(),
…
define_sweep<KLoopFullDomain>(
define_stages(
StencilStage<Lap, IJRange<cComplete,0,0,0,0> >()
)
)
…
);
for(int step = 0; step < 10; ++step)
{
stencil.Apply();
}
Update-function
lap(i,j,k) = data(i+1,j,k) + …
ENDDO
ENDDO
ENDDO
DO k = 1, ke
DO j = jstart, jend
DO i = istart, iend
Stencil Setup

## Slide 8: Pros and Cons of the approach
Pros
Performance and portability
Better separation of implementation strategy and algorithm
The library suggest / forces certain coding conventions and styles
Cons
It is not a free lunch maintenance is necessary
   Adding support for new hardware platforms
   Implementation of library extensions e.g. indirect addressing

## Slide 9: Single-node performance
CPU / OpenMP Backend
Factor 1.6x - 1.7x faster than the COSMO dycore
No explicit use of vector instructions (10% up to 30% improvement)
GPU / CUDA backend
Tesla M2090 (GPU with 150 GB/s memory bandwidth) is roughly a factor 2.6x faster than Interlagos (CPU with 52 GB/s memory bandwidth)
Ongoing performance optimizations
Chart: Speedup
| GPU HP2C (Tesla M2090) | CPU HP2C (Interlagos) | CPU Fortran (Interlagos)
Speedup | 4.16 | 1.6 | 1

## Slide 10: Conclusions
Stencil Library
Single source code
Domain specific language abstracting stencil definition
Performance portable code running on CPU and GPU
Integration with COSMO
Multi node support based on GCL
Wrapper providing a Fortran interface for the HP2C dycore
Important steps towards production
Interested?
3 to 4 day workshop during the first week of December @ BTZ Langen