## Slide 1
COSMO PP CITTA' Meeting
COSMO GM 2025, Basel, Switzerland
www.cmcc.it
CMCC contribution to PP CITTA’: What we’ve accomplished so far, what lies ahead
A. Campanale, J.-P. Schulz, M. Adinolfi, M. Raffa, P. Mercogliano

## Slide 2
To prove the validity of the implementation, the results have been compared against the COSMO model and observations
The period of interest is the summer 2017, the third hottest summer in the Italian history.
ROME
MILAN
The selected cities are the two biggest Italian urban clusters, Rome and Milan.
What we’ve accomplished so far
UHI over Rome and Milan during a summer period

## Slide 3
What we’ve accomplished so far
Simulation setups: COSMO vs ICON
Computational domains adopted for both models, ICON and COSMO, in blue, IFS boundary conditions domain in red.
Model | ICON v2.6.6 | COSMO v6
Boundary forcing | IFS (8.5km) for IC and BCs (at 6hr) | IFS (8.5km) for IC and BCs (at 6hr)
Horizontal resolution | 2.5km | 2.2km
Land surface model | Multi-layered tiled TERRA | Multi-layered TERRA
Land use dataset | GLC2009 | GLC2009
Period | 01-31 August 2017 | 01-31 August 2017
Simulations | TERRA_URB activated (TU_ON) / TERRA_URB deactivated (TU_OFF) | TERRA_URB activated (TU_ON) / TERRA_URB deactivated (TU_OFF)
For both cities, the same Impervious Surface Area (ISA) was used for both models to ensure comparability, as ISA is the key parameter for TU
More details on the experiments can be found in Campanale, A. et al. (2025)
ROME
MILAN
What we’ve accomplished so far

## Slide 4
What we’ve accomplished so far
What we’ve accomplished so far
MILAN
ROME
Without TU, both models cannot capture the urban-rural anomaly,
leading to a strong cold temperature bias!
Spatial distributions of urban-rural anomaly
ICON
COSMO
COSMO
ICON

## Slide 5
What we’ve accomplished so far
What we’ve accomplished so far
Urban Heat Islands and diurnal cycles
Without TU, both models cannot capture the sub-daily dynamics of UHIs!
Campanale, A. et al. (2025). Investigating urban heat islands over Rome and Milan during a summer period through the TERRA_URB parameterization in the ICON model. Urban Climate, 60, 102335.

## Slide 6
What we’ve accomplished so far
What we’ve accomplished so far
Main events / periods of interest for the analysis
1x Heatwave (7-13 Aug 2020), characterised by:
    Maximum temperatures ~38°C, average mean temperatures ~33°
    8-days long heatwave (one of the
    longest in Paris history)
1x Convective event / thunderstorm (9-10 May 2020)
    Precipitation: 35.6 mm (night of 9 May) + 15.2 mm (10 May).
    Windspeed peak: 63.7 km/hr
FPS URB-RCC aims to understand the impact of urban areas on regional climate.
EURO-CORDEX (12 km) domain (ERA5 driven)
CP domain (3km)
Analysis domain
ERA5 ~31km
EURO-CORDEX
domain 12km
Convection-Permitting
domain 3km
Urban Fraction of Paris
Addressing the urban climate change in the CORDEX community

## Slide 7
What we’ve accomplished so far
PARIS stations used for 2m temperature
UHI = Urban temperature – Rural Temperature
ICON newly coupled with TERRA_URB is one of the best performing models in the CORDEX ensemble
Addressing the urban climate change in the CORDEX community

## Slide 8
What we’ve accomplished so far
PARIS stations used for 2m relative humidity
UDI = Urban rel. humidity – Rural rel. humidity
Addressing the urban climate change in the CORDEX community
ICON newly coupled with TERRA_URB is one of the best performing models in the CORDEX ensemble

## Slide 9
BOLOGNA Case study area
Regional climate Model: ICON-CLM
Urban Model: TERRA_URB (Wouters et al., 2016; Campanale et al., 2025)
Resolution: 2.5km (0.0225°)
Period: Year 2022 as spinup, Year 2023 as analysis period
    Forcing data: ECMWF ERA5 reanalysis.
    Urban Fraction: From urban class of GLC2009, with possibility of smoothing
Reference observational dataset: ERG5 5.5km, Antolini et al., 2015
Reference configuration: ICON-D2
Variable validated: 2m temperature and 2m relative humidity for UHI and UDI calculation against ERG5 dataset (Antolini et al, 2015). MAE and RSME considered metrics.
Urban-Rural mask: ISA >= 0.3 classified as urban point, otherwise as rural point
Urban coverage of the entire ICLM computational domain
Urban Fraction (ISA) and Urban-Rural mask of Bologna in ICLM
What we’ve accomplished so far

## Slide 10
As expected, no Urban Heat Island (UHI) effect was observed for maximum temperature, while a UHI intensity of 1.5°C occurred during the night across almost the entire year of 2023
What we’ve accomplished so far

## Slide 11
Urbanized ICLM is able to accurately reproduce the daily dynamics of the UHI in all seasons, with only a slightly too warm daytime bias in DJF and, to a lesser extent, in MAM
DJF
MAM
JJA
SON
2023
What we’ve accomplished so far

## Slide 12
The model overestimates the UDI effect during the day, especially in DJF and MAM, while it provides a good representation at night, when the phenomenon is stronger
What we’ve accomplished so far

## Slide 13
Urbanized ICON accurately reproduces the daily dynamics of the UDI in JJA and SON, while it is too dry in DJF and MAM, leading to an overestimation of the UDI effect, especially during the day.
DJF
MAM
JJA
SON
2023
What we’ve accomplished so far

## Slide 14
UHI amplification factor defined as (Xue et al., 2023)
AUHI = UHI (HW) – UHI (noHW)
Summer 2023 experienced a record number of days with ‘extreme heat stress’
Two heatwave event in JJA 2023 have been selected:
09-19 July 2023
11 to 27 August 2023
Over Bologna the UHI effect, driven by the presence local urban morphology, represents a persistent vulnerability, present regardless of heatwave conditions. During heatwaves , urbanized ICLM tends to slightly overestimate UHI effect
HW
no HW
Amplification Factor
What we’ve accomplished so far

## Slide 15
What we’ve accomplished so far
Better representation of urban heterogeneity. Testing LCZs: At the moment, ICON is very well tuned to GLC2009, so introducing ECO-SG might initially worsen the results.
LCZs based on ECO-SG also in ICON, implemented by Jan-Peter Schulz (DWD, CMCC)

## Slide 16
What lies ahead
The COSMO Priority Project CITTA’ is very successful!
The bulk urban parameterization TERRA_URB, well established in the COSMO model, was implemented by Jan-Peter Schulz (DWD, CMCC) in its successor, the ICON model. This newly urbanized version of ICON effectively captures key urban meteorological features across different case study areas - even outperforming more sophisticated models at the mesoscale.
Some food for thought on what we can still improve:
Testing of LCZs: Explore whether a more heterogeneous urban canopy parameter representation improves ICON's performance.
Assessing the coupling between heatwaves and urban heat islands (UHI): How do these phenomena interact in ICON simulations?
Applying the model at climate timescales: Will UHIs intensify under future climate scenarios?
Increasing the resolution of UHI representation: Either by refining the ICON resolution of our simulations or by using ICON output as forcing data for hectometric-scale models.

## Slide 17
www.cmcc.it
Thank you for your attention,
questions or any suggestions?
angelo.campanale@cmcc.it