## Slide 1
Yoav Levi and Pavel Khain
COSMO PP CITTA‘ Sep. 2025
CITTA status at IMS
COSMO GM 2025, Basel

## Slide 2: Previously on Città
The urban parametrization is operational since 30.7.2023.
2 identical hindcast runs one with urban parametrization and the other without for the year 2024.
Due to reproducibility problem it is difficult to compare.
Wind verified against upper air Lidar observation in Jerusalem.
COSMO GM 2025, Basel

## Slide 3
Is there a reproducible problem?
Low correlation over the sea ->
suspect INTEL + OPEN-MP on ATOS
may bias the results
Non-Urban
COSMO GM 2025, Basel

## Slide 4: Intel (Uli) ecRad with OMP
COSMO GM 2025, Basel

## Slide 5: Solution: Remove the OMP from ecRad
substitute all !$OMP -> ! !$OMP in these files (add exclamation mark):
atm_phy_nwp/mo_nwp_ecrad_interface.f90
externals/ecrad/radiation/radiation_save.F90
For output:
src/io/shared/mo_name_list_output.f90
src/io/shared/mo_post_op.f90
src/io/shared/mo_util_cdi.f90
src/include/omp_definitions.inc does not work
Final tuning is still required
COSMO GM 2025, Basel

## Slide 6: experiments
 | nodes | Reproducible | Run time | Ratio | SBUs | Ratio
Intel+openMP | 4 | NO | 00:04:13 | 1 | 613.99 | 1
GNU w/o openMP | 4 | yes | 00:13:05 | 3.10 | 1905.06 | 3.1
GNU+openMP | 4 | yes | 00:05:51 | 1.39 | 851.82 | 1.39
Intel w/o openMP | 4 | yes | 00:08:51 | 2.11 | 1288.65 | 2.1
Intel threads-per-core=1 | 8 | NO | 0:03:02 | 0.71 | 883.37 | 1.42
Intel+openMP | 1 | NO | 00:20:18 | 4.81 | 738.971 | 1.20
Intel+openMP RRTM | 4 | yes | 0:03:58 | 0.94 | 577.586 | 0.94
Intel ecrad w/o OpenMP | 4 | yes | 0:04:39 | 1.10 | 677.086 | 1.10
Intel-llvm (Uli) + openMP | 4 | NO | 0:04:06 | 0.97 | 597.001 | 0.97
Intel-llvm ecrad w/o OpenMP | 4 | yes | 0:04:46 | 1.13 | 694.074 | 1.13
Intel-llvm (Matan) ecrad w/o OpenMP | 4 | yes | 0:04:15 | 1.01 | 626.123 | 1.02
COSMO GM 2025, Basel

## Slide 7: Urban vs. no Urban
COSMO GM 2025, Basel
Sigalit Berkovic
Urban parametrization increases the average wind speed by less than 0.5 m/s
most of the effect at the lowest level at night. The sea breeze?
2 km

## Slide 8: Temp. Verification Bet Dagan sonde
Jan. night ---
Jan. day
Feb.
2 km
Mostly negative bias that increase with height
Sigalit Berkovic
COSMO GM 2025, Basel
1 km

## Slide 9: Wind Speed Verification
COSMO GM 2025, Basel
Jan. night ---
Jan. day
2 km
During the day +~0.5 m/sec bias ->
Increase Zo
Sigalit Berkovic
1 km

## Slide 10: Z0 and paved fraction
COSMO GM 2025, Basel
Z0 in DOM01.extpar.nc
FR_PAVED NEW
FR_PAVED GlobCover
Z0 Looks like FR_PAVED GlobCover (non urban)
If Z0 was not changed by mistake we discovered the city breeze

## Slide 11: UHI induced city breeze
COSMO GM 2025, Basel
Similar average wind speed
Rural desert
Jerusalem
Average city breeze = 0.05 m/s (1.7%)

## Slide 12: Urban effect on Wind Speed
COSMO GM 2025, Basel
Similar average wind speed
Sea
Tel Aviv
Average city breeze = 0.08 m/s (3.7%)

## Slide 13: Did we find a measure for the city breeze?
COSMO GM 2025, Basel

## Slide 14: Summary
COSMO GM 2025, Basel
Should we use Ecoclimap-SG for correct Z0 in urban areas?
Next?

## Slide 15: Thanks for the attention
COSMO GM 2025, Basel

## Slide 16: Wind Speed Verification
COSMO GM 2025, Basel

## Slide 17
Classes 27, 28, 29, 32 are partially urban. Taking them as 1 leads to overestimation in Urban fraction
ECOCLIMAP-SG (300m resolution)
Carmela Apreda (CMCC)
Roni Drori (IMS)
Urban classes 24-33
↓
GlobCover class 19
on triangular grid
FR_PAVED NEW
sea