## Slide 1: COSMO PP IMPACT ICON on Massively Parallel ArChiTecture
X. Lapillonne, C. Osuna MeteoSwiss
V. Clement3, O. Fuhrer1,, C. Osuna1, K. Osterried3, H. Vogt2 , A. Walser1 , C. Charpilloz1, P. Spoerri3 , T. Wicky
1MeteoSwiss, 2CSCS, 3C2SM ETH

## Slide 2: Why investing a new HPC project ?
Physical limits , Moore’s law is over
  2004 end of frequency scaling  multi-core
  2012 end of rapid cost decline  constant $/transistor
  2019 heat dissipation constraints  massively parallel architecture
  2021 end of reduction in feature size  ?
Specialized hardware, large diversity
increased on chip parallelism
GPUs
Many-core
processors
AI Accelerators
(e.g. Google Tensor Flow, Intel Nervana)
FPGAs
K. Flamm 2017, IEEE Computing in Science & Engineering
Vector
??
Unknown

## Slide 3: New HPC project
Build on know-how from POMPA project
Future HPC will show ever more parallelism than actual GPU & CPU:
    further adapt our models and programming tools
    Investigate tasks parallelism
Focus on ICON model

## Slide 4: COSMO PP IMPACT (submitted) ICON on Massively Parallel ArChiTecture
First implementation of a baseline OpenACC version of ICON for NWP :
  Initial version of the dycore is available
  Physical parametrizations require a full port
Investigate OpenMP 4.5 for accelerator (currently not mature enough in all compilers)
Improve modularity of the model structure
Need to invest in software engineering beyond OpenACC in order to make support of different platforms maintainable in the long term:
  Implement ICON Dycore based on DSL (Domain Specific Language)
  evaluate use of CLAW-DSL abstractions for the physical parameterisation
  Investigate task parallelism
Low risk, known technologies
High risk
High potential Future proof

## Slide 5: Performance portability, why do we need abstraction ?
Directives : portable but not optimal code with single source
  different optimization for different target architecture
  in the dynamics difficult to achieve opt. performance
Chart: 
| Radiation (Phy), OpenACC | Hor. Diff (Dyn), OpenACC vs STELLA
Base | 1 | 1
Opt | 0.74074 | 0.55556
x1.3
x1.8
Possible solutions : Domain specific Language (Gridtools), abstraction, CLAW

## Slide 6: CLAW Fortran manipulation tool
https://github.com/claw-project
CLAW FORTRAN Compiler
  OpenSource project, developped by MeteoSwiss/ETH.
  Based on the OMNI Compiler (developed by Riken)
Two modes
CLAW-directives
  Transformation in exisiting CPU optimize code with pre-existing OpenACC directives
CLAW-DSL (single column abstraction for the physics)
  Code written has single column (abstract horizontal direction)
  OpenACC/OpenMP directives are automatically added depending on the target (abstraction)

## Slide 7: CLAW-DSL Single column abstraction approach : performance portability in the Fortran physics
Separation of concerns
  Domain scientists focus on their problem (1 column, 1 box)
  CLAW compiler produce code for each target and directive languages

## Slide 8: Claw one column example
!$claw parallelize forward
DO icol = 1, ncol
CALL lw_solver(ngpt, nlay, tau(icol,:,:))
END DO
CALL lw_solver(ngpt, nlay, tau)
SUBROUTINE lw_solver(ngpt, nlay, tau, …)
  !$claw define dimension icol(1:ncol) &
  !$claw parallelize
  DO igpt = 1, ngpt
  DO ilev = 1, nlay
tau_loc(ilev) = max(tau(ilev,igpt) …
Loop over horizontal direction generated by claw at compile time

## Slide 9: High level DSL for weather and climate
Increase abstraction : no explicit data structure, loops, HW-dependent details
More optimizations, task parallelism
Higher productivity and code safety
Language still to be defined, developer input required
Collaboration with ECMWF as part of ESCAPE project
Example gtclang
(working implementation of the COSMO dycore)
gtclang language prototype :
Generates efficient code for x86 multi-core,NVIDIA GPUs, Intel Xeon Phi
4x – 6x reduction in LOC

## Slide 10: High level Intermediate Representation (HIR)
Multiple high level DSL (different communities)
Single HIR and optimization tool chain - currently based on GridTools Framework, Joint development between CSCS / MeteoSwiss / C2SM
CLAW-DSL : Fortran DSL for the physical parameterizations

## Slide 11: Thanks you

## Slide 12: GridTools Framework
“SDK for weather and climate science”
Joint development between CSCS / MeteoSwiss / C2SM
Domain-specific for Earth system model components
Regional (production) and global grids (prototype)
Multiple APIs (C++, Python, gtclang)

## Slide 13: Claw one column example
!$claw parallelize forward
DO icol = 1, ncol
CALL lw_solver(ngpt, nlay, tau(icol,:,:))
END DO
CALL lw_solver(ngpt, nlay, tau)
SUBROUTINE lw_solver(ngpt, nlay, tau, …)
  !$claw define dimension icol(1:ncol) &
  !$claw parallelize
  DO igpt = 1, ngpt
  DO ilev = 1, nlay
tau_loc(ilev) = max(tau(ilev,igpt) …
Loop over horizontal direction generated by claw at compile time

## Slide 14: Efficiency myth
Heavily optimized code is faster than Fortran + OpenACC
(Example: 1.5x for horizontal diffusion operator)

## Slide 15: Software (Automatic optimization)
Compilers will not solve the problem!
DSL-based code can be automatically optimized for a specific hardware target
E.g. “Design of a Compiler Framework for Domain Specific Languages for Geophysical Fluid Dynamics Models” (Fabian Thüring, MSc thesis)
Example: Fast-waves solver
Graph representation of code
Rearrange for data-locality
Run independent computations in parallel

## Slide 16: STELLA SYNTAX
Only specify neighbourhood relations and domain of application
Code for specific architecture is generated at compile time

## Slide 17: COSMO quasi-global
Dx | # nodes | SYPD | MWh / SY
0.93 km | 4,888 | 0.043 | 596
1.9 km | 4,888 | 0.23 | 97.8
3.7 km | 4,888 | 0.97 | 20.8
Source: Vogt, 2017
What would it take to do a 36 year AMIP simulation?
 | Dx = 0.93 km | Dx = 1.9 km
Time to solution | 840 days | 156 days
Energy to solution | 22 GWh (0.9 M$) | 3.5 GWh (0.150 M$)
CO2eq to solution | 3’800 tons | 640 tons
$ to solution (2go.cscs.ch) | 97 M node hours  68 M$ | 18 M node hours  12 M$

## Slide 18: Ensemble prediction
The atmospheric system is a chaotic system: i.e. high sensitivity to initial condition
Initial conditions (dotted lines)
Initial conditions (full lines)
Operational 120 h forecast
Modified forecast

## Slide 19: Modeling the Earth system
(source https://www.ecmwf.int/sites/default/files/medialibrary/2017-09/atmospheric-physics-754px.jpg)
Notes: Earth system is a multi-scale, multi-physics problem.
Many different procceses act together that have to be represented in one form or another in a weather and climate model.
Formation and dissipation of different types of clouds.
Interaction of the radiation impinging from the sun, and the longwave radiation emmanating form the warm Earth.
Surface-vegation-atmosphere-transfer determining the latent, sensible fluxes of heat.
But also the effect of topogrphy on the atmosphere that acts on the momentum budget.
So let’s take for example a deep cumulus cloud…