## Slide 1: COSMO-LEPS Ensemble verification scores
SON25-MAM26
Dimitra Boucouvala

## Slide 2
COSMO-LEPS ensemble verification (20 members) started in SON25 (7 km resolution) over European domain with MEC /FFV2 software (in ATOS machine)
Notes: Cosmo leps verification is performed over this domain with 20 members and 7km resolution using MARS and FFV2 and it runs on atos machines

## Slide 3
https://www.cosmo-model.org/content/tasks/verification/default.htm
Notes: This is the website where you can view the scores by clicking on ‘surface parameters’ geographical plots or time series

## Slide 4
2m temperature
SON 25
DJF 26
MAM 26
Worse scores at night and MAM season
Notes: CRPS (Continuous ranked probability score) and spread skill ratio for the 3 seasons. The CRPS is higher at night (EPS more difficult to predict minimum values ) and the same time it becomes underdispersive

## Slide 5
SON 25
DJF 26
MAM 26
10m Wind Speed
Similar error for all seasons
Notes: The error is similar all 3 seasons . Diurnal difference only for spread/skill (worse values at night)

## Slide 6
2m Dew point Temperature
SON 25
DJF 26
MAM 26
Worse scores in the day and MAM season
Notes: In Td2m the errors are higher in the day as it is shown on CRPS and spread/skill graphs

## Slide 7
Total Cloud Cover
SON 25
DJF 26
MAM 26
Worse scores at night and MAM season
Notes: Scores worse at night

## Slide 8
2m temperature (CRPS time series)
DJF 26
Better score in the day and February
Night
Day
Notes: These graphs of CRPS are for the whole season of winter 26 and February was the better score for day and night

## Slide 9
MAM 26
Reliability Diagrams 6h precipitation
(0.1, 1, 5mm thresholds)
DJF 26
SON 25
Overforecast in higher thresholds
Notes: Overall, the forecasts show reasonable reliability for the lower rainfall threshold. As the rainfall threshold increases, the reliability decreases, with a tendency to overpredict the probability of more intense rainfall events. The larger deviations from the diagonal at higher thresholds may also be associated with the smaller sample size of these relatively rare events.” the score is worse in MAM

## Slide 10
SON 25
ROC Area 6h precipitation (0.1, 5, 10mm threshold)
DJF 26
MAM 26
Notes: Overall, the system shows good skill in detecting rainfall events. The ROC-AUC decreases as the rainfall threshold increases, indicating lower overall discrimination for more intense rainfall. However, these higher thresholds represent rarer events with fewer samples, so the decrease in AUC should be interpreted with caution.

## Slide 11
CRPS spatial variability map T2m (DJF26-36h)-Geographical Plots
Notes: You can view the errors spatial variability

## Slide 12
Scores over Greek Domain
Tendency similar to the whole area but errors slightly higher
Notes: Scores are also produced over Greek domain. The tendency is the same as the big domain but the errors are slightly higher

## Slide 13
Conclusions-Next steps
Some COSMO-LEPS ensemble scores are presented.
Scores are generally worse in MAM season and night
Wind speed scores similar for 3 seasons.
JJA26 season will be added soon
Common Area plots can also be produced.
COSMO-LEPS will be replaced by ICON-LEPS ?
Thank you !