## Slide 1: Andrzej Mazur (on behalf of Andrzej Wyszogrodzki) COSMO General Meeting 2026
NWP/HPC @ IMGW-PIB
status and plans

## Slide 2
2 IMGW-PIB locations:
Warsaw 1Pf CPU (Dell PowerEdge R660 / Intel® Xeon® Platinum 8480+ 2.0G)
180 nodes x 2 CPU x 56 cores = 20160 cores, 512GB RAM/node
Krakow 0.75 Pf GPU (3 nodes of Dell PowerEdge XE9680)
3 x 2 x Intel® Xeon® Platinum 8468 2.1G, x 48 cores = 288 CPU corers
3 nodes x 8 cards NVIDIA HGX H100 8-GPU = 24 GPU cards
1024 Gb RAM/node
0.25 Pf CPU (Dell PowerEdge R660 , Intel Xeon Platinium 8480+ 2.0G)
45 nodes x 2 CPU x 56 cores = 5040 cores, 512GB RAM/node
Storage: 2x 4 PB datastore
GPU possible applications: COSMO/ICON, hydro models,
ALADIN/Destination Earth
World Bank PODPOW project (10+ mln EURO) run from 2025+
HPC for 2025+

## Slide 3
2026 NWP operational deterministic models
COSMO 14k0
COSMO 7k0
COSMO 2k8
ICON-LAM 2k5
Model Version | COSMO14k 5.05 | COSMO 7k V 6.01 | COSMO 2k8 V 6.01 | ICON-LAM (2024.03)
Grid spacing | 14km | 7km | 2.8km | R2B10,2.5k
Grid size [NxMxL] |  | 415x445x51 | 380x405 x 41 | 294638 x 65
Integration time [sec] | 55 | 40 | 15 | 24
Forecast length [hours] | 78 | 96 | 60 | 48
Forcst time start [UTC] | 00,06,12,18 | 00,06,12,18 | 00,06,12,18 | 00,06,12,18
IC/BC / update time [h] | ICON / 3h | ICON / 3h | COSMO7k0/1h | ICON / 3h
R2B10, ~2.5km
14 x 14 deg domain,
294636 elements
rotated north pole: -170,0,0
65 levels, dt=24s
48 hour forecast
4x/day (00, 06, 12, 18 UTC)
Changes planned
Increase resolution to ~1km (it is running, tho’ not operationally yet)
Nested subdomains at hectometric scale (500m and below)
ECOCLIMAP-SG + TERRA_URB

## Slide 4
ICON-PL
(dated 2024.03, 2.5km, includes cp/cv bug fix, the RRTM radiation scheme)
COSMO-CE-PL
(v. 6.01, 2.8km)
Verification using MEC/Rfdbk ( CARMENs)
Comparison with the Polish SYNOP (Poland domain), TEMP stations (Poland stations)
ICON-LAM vs COSMO
Exceptions (still under investigation…):
There is a systematic difference in wind speed and wind direction biases between ICON-PL and COSMO-CE-PL
ICON-PL produces more rain than COSMO-CE-PL during convective seasons
ICON-PL is generally less accurate than COSMO-CE-PL at the top of the atmosphere for all analyzed parameters
ICON-PL overall performs better than COSMO-CE-PL for most of surface and upper air parameters
Notes: 4

## Slide 5
ICON -> COSMO 7km
products
verification
statistical postprocessing
PERTURBATIONS:
C-Soil, T_SO
Soil physics
IC/BC
TLE ensemble system 2025+
TIME LAGGED EPS / COSMO 2k8 (20 members)
Changes planned
COSMO -> ICON-LAM transition
Perturbation setup -> increase spread

## Slide 6
RUC - Rapid Update Cycle
Control FIR zones
Turbulence, icing, visibility, convective parameters
COSMO 2.8km
1h analysis
3h forecast
30 min update (48/day)
assimilation:
Opera radar SRI, AMDAR and telemetric 380 stations
Applications:
aviation,
nowcasting
flash flood
  Changes/additions (as planned):
  Opera (15 min) → RainGRS+ (5/10 min)
  2-moment microphysics (graupel and hail) – to be running operationally soon

## Slide 7
POLRAD+ NETWORK
Doppler /dual-polarized radar data: Poland (8) + Lithuania (2), Ukraine (1), Slovakia (4), Czech Republic (2), Germany (4)
NETWORK OF TELEMETRIC RAIN GAUGE STATIONS (491)
METEOSAT SATELLITES
RainGRS composites
multi-source GRS precipitation fields
data quality control,
weighted processing of precipitation inputs
RainGRS+OPERA, PWS*), CML**)
POLRAD + OPERA
RUC - Rapid Update Cycle
*) Personal Weather Stations
**) Commercial Microwave Links – point-to-point radio connections between cellular base stations that double as high-resolution environmental sensors.

## Slide 8
Regional climate simulations with ICON-CLM
Contribution to EURO-CORDEX
CMIP6 GCM: NorESM2-MM
Scenarios: SSP126, SSP370
UDAG project (Updating the Data basis for Adaptation to climate change in Germany) – tune ICON-CLM at 3 km on DKRZ
Configuration Optimization of ICON-CLM 12km over Europe and 3km over Germany using a Linear Meta MOdel (LiMMo)

## Slide 9
COSMO sci. projects 2025/2026
PP APOCS (Application of Personal Weather Station and Opportunistic Sensor Data CrowdSourcing) running
PP KAOS (Addressing the complexity in the weather forecast) running
PP PROPHECY ( PRObabilistic Prediction at High-resolution with EnhanCed perturbation strategY)  finished.
PP CITTA (City Induced Temperature change Through A’dvanced modelling)  finished
PT EGALITE (Early warninG and AnaLysIs SysTEm for release and dispersion of contaminants)  finished (publication prepared and submitted).
PP CARMENs (Cosmo Application of Rfdbk/MEC on ENS)  finished

## Slide 10
PP APOCS (Application of Personal Weather Station and Opportunistic Sensor Data CrowdSourcing)
280+
active PWS stations
radius · 52°N / 19°E
500 km

## Slide 11
PP APOCS – Task 1: Development of COSMO PWS database
The first tests with employee devices and the test database (approx .40 stations)
Include a larger number of stations for internal tests
Add participants from COSMO partners and other collaborating institutions.
Include data QC software and web based GUI with visualization

## Slide 12
PP APOCS – Task 2.1: Adaptation of the RainGaugeQC system
to CML-based precipitation data)

## Slide 13
PP APOCS – Task 4.3: Application of PWS
to NWP model verification in urban areas

## Slide 14
PP KAOS: perturbation of the soil variables
Temperature shift as a function of soil depth, based on Tsyrulnikov et al. (2023).
The soil temperature perturbation scheme is tested on the test cases with inversion favorable conditions.
Example: aggregated spread for Siedlce station.
as a part of PP KAOS, we are working on the development of a new scheme for introducing soil temperature perturbations
the scheme has been implemented and tested in ICON on a number of test cases with inversion favorable conditions
we are planning to add and test more soil-related variables

## Slide 15
PP KAOS: cloud microphysics parameters for SPP development
warm-rain process | single-moment | double-moment
accretion |  | 
selfcollection | N/A | 
breakup | N/A | 
warm-rain process | single-moment | double-moment
accretion |  | 
selfcollection | N/A | 
breakup | N/A | 
Reproduction of Figure 10. from Niquet et al. (2024), used to derive perturbation ranges
for , and parameters.
Reproduction of Figure 9. from Long (1974), used to derive perturbation ranges for parameter.
as a part of PP KAOS, we are working on the development of the SPP method in ICON
recently, we have derived perturbation ranges for several parameters related to single- and double-moment cloud microphysics
we are planning to test them in an ensemble setup

## Slide 16
PP KAOS: Time-Lagging Ensembles
To reduce computational cost: skip the MVE part, stick with TLE  the number of elements = 10. An appropriate "base" models (deterministic, but with a sufficiently long forecasting period; 90 hours). Remember the previous forecasts…
youngest
oldest
Spread-Skill charts; TD2M, ”Super(TL)ensemble”, 60 members
Standard mean Weighted mean Standard regression Weighted mean Weighted mean ANN-based mean
(regression+geo.coords) (regression+orography)
Spread-Skill charts; TD2M, ”Super(TL)ensemble”, 50 members

## Slide 17
Dry Convective Boundary Layer Revisited Mixed Layer Scaling G.Cegielski, G.Zakrzewski, A.Wyszogrodzki, A.Jaczewski, W.Interewicz
Configurations
Varying surface heat flux
Varying resolution
Closure model: LES (Smagorinsky) vs. NWP (Raschendorfer)
peiodic
LES
Raschendorfer
CASE STUDY: Dry Convective Boundary Layer (DCBL)
peiodic

## Slide 18
LES RESULTS: PROFILE SCALING W. DIFFERENT SCALES
IMPACT OF RESOLUTION AND TURBULENCE MODEL
Scaled Resolved
Turbulent Heat Flux: Varying BC
Buoyancy and Buoyancy Flux
Buoyancy Variance and Eddy Viscosity

## Slide 19
Planned (other) activities (applications)
Support for General Aviation, i.a. non-engine aircraft users based on numerical forecasts, with particular emphasis on the description of convection on a local/regional scale
Notes: 19